## Slide 1: Why use ferrules and how to apply them correctly…
Maria Schierscher, Associate Product Marketing Manager – Industrial Tools

## Slide 2: What is a ferrule?
Why you should use ferrules….
Copper tube that is tin plated with a nylon insulation
Sizes: 250MCM to 28 AWG
Styles:
Single – for use with one wire
Twin – for use with two wires
Strips – for use with specific hand tools
Reeled – for use with semi-automatic devices
Reeled ferrules for the CF3000
Twin (double) ferrules
Ferrule kits

## Slide 3: Why are ferrules used?
Why you should use ferrules….
Solid Connection
  strengthen stranded wire bundles
  elimination of stray strands
Ease of installation
Long term electrical performance
  Airtight
  Corrosion resistance
Durability and safety of the connection
  vibration resistance
  avoidance of higher temperatures, short-circuits, and arc flashes
  shape and integrity retention with removal and reinsertion
Twin ferrules allow simultaneous insertion of two wires
Required in Europe for CE certification
High quality, carefully designed and built panel

## Slide 4: Cutting the wire correctly matters
Why you should use ferrules….
Be sure to not damage the wire when cutting.
Incorrect cut: Bite cut, squeezing the wire
Correct cut: Shear cut

## Slide 5: Choosing the correct wire stripping tool matters
Why you should use ferrules….
WIREFOX – 10 1212150
WIREFOX-E 10 1212706
34-8 AWG
WIREFOX – 4 1212159
WIREFOX-E 4 1212704
28-12 AWG
WIREFOX – 6SC 1212158
WIREFOX-E 6SC 1212705
16-8 AWG
WIREFOX – 16 1212155
WIREFOX-E 16 1212707
12-5 AWG
Flat blade
V-blade
Oval blade

## Slide 6: Stripping the wire correctly matters
Why you should use ferrules….
Be sure to not damage the strands or insulation when stripping the wire.
Incorrect strip:
Correct strip:

## Slide 7: Choosing the correct crimping tool matters
Ferrule crimpers vary by
AWG range
Crimp profile
Open or nested
Front or side entry
Length of the handle
CRIMPFOX DUO 16S 1202877 26-6 AWG single
2 x 20-10 twin
CRIMPFOX CENTRUS
6H NC 1202883 24-10 AWG
6S NC 1202882 24-10 AWG
10H 1213156 24-8 AWG
10S 1213154 24-8 AWG
CRIMPFOX 25R 1212039 8-4 AWG
CRIMPFOX 50R 1212041 2-1 AWG
Why you should use ferrules….

## Slide 8: Crimp Profiles…Which one should I use?
Why you should use ferrules….
Crimp profiles are based on user and application preference
  Conductor must be prepared correctly
  Contact and conductor must be compatible
  Conductor must be positioned correctly in the contact
  Suitable crimping tool must be used
WM Crimp
B Crimp
Hex Crimp
Square Crimp
Indent/prong Crimp
Double indent Crimp
Oval Crimp
Trapezoid Crimp

## Slide 9: Or automate the crimping
Why you should use ferrules….
CF 3000 1205516
20-14 AWG dies included
22 AWG kit 1212376
CF 1000-1,5 1208199 22-12 AWG
20-16 AWG dies included
CF 1000-10 1212456 12, 10, 8 AWG
No dies included

## Slide 10: How to apply a ferrule
Why you should use ferrules….
Flush cut the conductor
Using a suitable wire stripper, strip the insulation off the conductor
Insert the stripped conductor into the plastic collar
The strands should completely fill the ferrule’s barrel and protrude no more than .02” (0.5mm)